## Slide 1: A Survey on Low Power Network Protocols for the Internet of Things based on a paper by: Rault et al
By: Noam Major, Elad Hillel, Itai Sidnik

## Slide 2: Presentation Overview
IoT Energy Challenges
The Importance of Low-Power Network Protocols
Energy Consumption in IoT Networks
Categorization of Low-Power Protocols
MAC Layer Protocols
Network Layer Protocols
Application Layer Protocols
Cross-Layer Approaches
Future Directions
Conclusion

## Slide 3: IoT Energy Challenges
Massive Scale: Billions of connected devices
Deployment Locations: Often remote or inaccessible
Cost Sensitivity: Energy efficiency directly impacts economic viability
Battery Constraints:
  Limited capacity
  Difficult/costly battery replacement
  Need for years of operation

## Slide 4: Why Network Protocols Matter
Communication dominates energy consumption:
  60-80% of total energy budget in typical IoT devices
  Far exceeds sensing and processing energy costs
Key Energy Drains:
  Transmission power
  Idle listening
  Protocol overhead
  Collisions and retransmissions

## Slide 5: Energy Consumption Breakdown
Transmission: Active sending of data packets
Reception: Receiving and processing incoming data
Idle Listening: Monitoring channel for potential transmissions
Overhearing: Processing packets meant for other nodes
Protocol Overhead: Control packets, beacons, synchronization

## Slide 6: Categorization of Low-Power Protocols
By Network Layer:
  MAC Layer (Media Access Control)
  Network Layer (Routing)
  Application Layer
  Cross-Layer Approaches
By Design Approach:
  Duty Cycling
  Data Reduction
  Energy-Efficient Routing
  Topology Control

## Slide 7: MAC Layer Protocols - Overview
Primary Goal: Efficient channel access
Key Energy-Saving Approaches:
  Duty cycling
  Collision avoidance
  Overhearing prevention
  Message passing optimization

## Slide 8: MAC Layer - Duty Cycling Protocols
Synchronized Protocols:
  S-MAC: Sleep/wake scheduling
  T-MAC: Adaptive duty cycle
  IEEE 802.15.4: Beacon-enabled mode
Asynchronous Protocols:
  B-MAC: Low power listening (LPL)
  X-MAC: Short preamble sampling
  RI-MAC: Receiver-initiated transmission

## Slide 9: MAC Layer - Performance Comparison
Metrics:
  Energy efficiency
  Latency
  Throughput
  Scalability
Trade-offs:
  Energy vs. latency
  Simplicity vs. performance
  Synchronization overhead vs. idle listening

## Slide 10: Network Layer Protocols - Overview
Primary Goal: Energy-efficient routing
Key Energy-Saving Approaches:
  Clustered architectures
  Multipath routing
  Geographic routing
  Data-centric routing

## Slide 11: Network Layer - Routing Protocols
LEACH: Low Energy Adaptive Clustering Hierarchy
  Cluster-based approach with rotating cluster heads
RPL: IPv6 Routing Protocol for Low-Power and Lossy Networks
  Destination-oriented directed acyclic graph (DODAG)
AODV-EE: Energy-Efficient Ad hoc On-Demand Distance Vector
  Energy-aware route selection
Geographic Routing: Position-based forwarding

## Slide 12: Network Layer - Energy-Saving Techniques
Clustering: Reducing communication distances
Data Aggregation: Combining multiple data packets
Multipath Routing: Distributing energy load
Sleep Scheduling: Coordinated with routing decisions
Topology Control: Adjusting transmission power

## Slide 13: Application Layer Protocols
CoAP: Constrained Application Protocol
  Lightweight alternative to HTTP
  Built-in resource discovery
  Observe option for reduced polling
MQTT: Message Queuing Telemetry Transport
  Publish-subscribe pattern
  Minimal packet overhead
  QoS levels for reliability/efficiency tradeoffs
AMQP: Advanced Message Queuing Protocol
  Reliable queuing with different delivery guarantees

## Slide 14: Protocol Stack Comparison
Traditional Internet: TCP/IP Stack
  HTTP, FTP, SMTP
  TCP, UDP
  IP
  Ethernet, WiFi
IoT Low-Power Stack:
  CoAP, MQTT
  UDP (typically)
  6LoWPAN
  IEEE 802.15.4, BLE, LoRaWAN

## Slide 15: Cross-Layer Approaches
Definition: Optimization across multiple protocol layers
Benefits:
  Coordinated sleep scheduling
  Joint routing and MAC optimization
  Application-aware protocol adaptation
Examples:
  DMAC: Data-gathering MAC
  CTP: Collection Tree Protocol
  TinyOS Low-Power Listening integration

## Slide 16: Real-World Protocol Performance
Case Study 1: Smart Agriculture Deployment
  Protocol: IEEE 802.15.4 + RPL
  Results: 2-year battery life, 99.8% reliability
Case Study 2: Building Energy Management
  Protocol: BLE + MQTT-SN
  Results: 45% energy savings over WiFi + HTTP
Key Findings: Proper protocol selection can extend device lifetime by 5-10x

## Slide 17: Emerging Low-Power Technologies
LPWAN: Low-Power Wide-Area Networks
  LoRaWAN: Long range, very low power
  Sigfox: Ultra-narrow band, subscription-based
  NB-IoT: Cellular-based IoT network
Wake-Up Radio: Ultra-low power secondary radio
  Eliminates idle listening
  Activation only when needed

## Slide 18: Future Research Directions
Opportunistic Energy Harvesting Integration
  Protocols adapting to available energy
Machine Learning for Protocol Optimization
  Predictive sleep scheduling
  Intelligent routing decisions
Secure Low-Power Communication
  Energy-efficient encryption
  Lightweight authentication
Standardization Challenges

## Slide 19: Conclusion
Network protocols dominate IoT energy consumption
Duty cycling is the most effective energy-saving technique
Protocol selection should consider application requirements
Cross-layer approaches offer the best optimization potential
Emerging technologies promise further efficiency improvements
Proper protocol design can extend IoT device lifetime from months to years